## Slide 1: UNIT-V
PIPELINING
&
VECTOR PROCESSING

## Slide 2: PIPELINING AND VECTOR PROCESSING
Parallel Processing
Pipelining
Arithmetic Pipeline
Instruction Pipeline
RISC Pipeline
Vector Processing
Array Processors

## Slide 3: PARALLEL PROCESSING
Parallel processing is a technique that is used to provide simultaneous data processing tasks for the purpose of increasing the computational speed of a computer.
Parallel processing is able to perform the concurrent data processing to achieve faster execution time.
Purpose of the parallel processing is to speed up the computer processing
capability and to increase the throughput.
  Amount of processing that can be accomplished during a given interval of time.
The amount of hardware increases with parallel processing and with it, the cost of the system increases.
Parallel processing can be viewed from various levels of complexity
  Lowest level  we distinguish between parallel and serial operations by the type of registers used(shift registers operate in serial fashion one bit at a time, while the registers with parallel load operate with all bits of word simultaneously)
  Higher level  multiplicity of functional units that perform identical or different operations simultaneously.

## Slide 4: PARALLEL PROCESSING
Parallel processing is established by distributing the data among the multiple
functional units.
For example arithmetic, logic and shift operations are separated in to three units.
The operations performed on the data in the processor is constitutes a data stream. The sequence of instructions read from memory constitutes an instruction stream.
Processor with multiple functional units are shown in fig below:
Adder- Subtractor
Integer multiply
Logic unit
Shift unit
Incrementer
Floating-point add-subtract
Floating-point multiply
Floating-point divide
Processor register
To memory

## Slide 5: PARALLEL PROCESSING
Flynn’s classification divides computers in to four major groups:
  Single Instruction stream, Single Data stream (SISD)
  Single Instruction stream, Multiple Data stream (SIMD)
  Multiple Instruction stream, Single Data stream (MISD)
  Multiple Instruction stream, Multiple Data stream (MIMD)
SISD represents the organization of single computer containing a control unit,
a processor unit, and a memory unit.
Instructions are executed sequentially and the system may or may not have internal parallel processing capabilities
Parallel processing in this case is achieved by pipeline processing or multiple
functional units.
SIMD represents an organization that includes many processing units under the supervision of a common control unit.
All processors receive the same instruction from the control units but operate on different items of data.
The shared memory unit must contain multiple modules so that it can communicate with all the processors simultaneously.
MISD structure is only of theoretical interest since no practical system has been constructed using this organization.

## Slide 6: PARALLEL PROCESSING
MIMD organization refers to a computer system capable of processing several
programs at the same time.
Most mutiprocessor and multicomputer systems can be classified in this category.
Flynn’s classification depends on the distinction between the performance of the control unit and the data processing unit.
One type of parallel processing that does not fit Flynn’s classification is pipelining.
Parallel processing computers are required to meet the demands of large scale computers in many scientific, engineering, military, medical, artificial intelligence, and basic research areas.
We consider parallel processing under the following topics like:
– Pipeline processing 
is an implementation technique where arithmetic
suboperations or phases of computer instruction cycle overlap in execution.
Vector processing  deals with computations involving large vectors and matrices.
Array processors  perform computations on large arrays of data.

## Slide 7: PIPELINING
Pipelining is a technique of decomposing a sequential process into suboperations, with each subprocess being executed in a special dedicated segment that operates concurrently with all other segments.
Each segment performs partial processing dictated by the way the task is partitioned.
The result obtained from the computation in each segment is transferred to the
next segment in the pipeline.
The final result is obtained after the data have passed through all segments.
One of the most important characteristic of pipeline is that several computations can be in progress in distinct segments at the same time.
The overlapping of computations is made possible by associating the register with each segment in the pipeline.
The registers provide isolation between each segment so that each can operate on distinct data simultaneously.
Pipeline organization will be explained with the help of the example as follows:
Let us assume that we want to perform the combined multiply and add operations with a stream of numbers.
Ai * Bi + Ci for i=1,2,3,4,…..,7

## Slide 8: PIPELINING
Each suboperation is to be implemented in a segment with in a pipeline.
Each segment has one or two registers and a combinational circuit as shown in fig below:
R1 through R5 are registers that receive new data with every clock pulse.
Multiplier and adder are combinational circuits. Suboperations performed in each segment of the pipeline are as follows:
R1
R2
Multiplier
R3
R4
Adder
R5
R1Ai, R2Bi R3R1 * R2, R4Ci R5  R3 + R4
Input Ai and Bi Multiply & input Ci Add Ci to product

## Slide 9: PIPELINING
In general any operation that be decomposed into a sequence of suboperations of about the same complexity can be implemented by a pipeline processor.
The technique is efficient for those applications that need to repeat the same task many times with different sets of data. The general structure of four segment pipeline is illustrated in fig as follows:
Operands pass through all four segments in a fixed sequence. Each segments consists of combinational circuit Si that performs suboperations over the data stream flowing through the pipe.
Segments are separated by registers Ri that hold intermediate results between the stages.
Information flows between adjacent stages under the control of common clock applied to all registers simultaneously.

## Slide 10: PIPELINING
The behavior of the pipeline is illustrated in the space time diagram as follows
•
Speed up of the pipeline is processing over processing is defined by the ratio
tn  time required to complete tasks by nonpipeline units to perform same operation.
K no. of segments.
tp  time required to complete tasks by pipeline units to perform same operations
an equivalent non-pipeline
ntn
(k  n 1)tp
Speedup 

## Slide 11: ARITHMETIC PIPELINING
Pipeline arithmetic units are usually found in very high speed computers.
They are used to implement floating point operations, multiplication of fixed-point numbers and similar computations.
A pipeline multiplier is essentially an array multiplier with special address designed to minimize the carry propagation time through the partial products.
Floating point operations are easily decomposed in to suboperations.
A pipeline unit for Floating point addition and subtraction is given as in the example as follows:
The inputs to floating point adder pipeline are two normalized floating point binary numbers.
X = A x 2a Y = B x 2b
A and B are two fractions that represents two mantissas and a and b are exponents.
Floating point addition and subtraction can be performed in four segments as in the figure as follows:

## Slide 12: ARITHMETIC PIPELINING
Register R is placed in between the segments to store intermediate results.
in
are four
Suboperations performed segments are :
Compare the exponents
Align the mantissas.
Add or subtract the mantissas
Normalize the result
The following numerical
example clarify the
suboperations performed
in each segment.
the
floating
two
point
Consider normalized numbers
X = 0.9504 x 103
Y = 0.8200 x 102
R
Compare exponents
by subtraction
b
R
Choose exponent
Exponents a
R
B
Align mantissa
Mantissas A
Difference
R
Add or subtract mantissas
R
Normalize result
R
R
Adjust exponent
R
Segment 1:
Segment 2:
Segment 3:
Segment 4:

## Slide 13: ARITHMETIC PIPELINING
The comparator, | shifter, adder-subtractor | , | incrementer | , | and
decrementer in | floating-point pipeline | are | implemented |  | with
The two exponents are subtracted in the first segment to obtain 3-2=1.
The larger exponent 3 is chosen as the exponent of the result. The next segment shifts the mantissa of Y to the right to obtain
X = 0.9504 x 103
Y = 0.0820 x 103
This aligns the two mantissas under the same exponent. The addition of the two mantissas in segment 3 produces the sum Z = 1.0324 x 103
The sum is adjusted by normalizing the result so that it has a fraction
with a non zero first digit.
This is done by shifting the mantissa once to the right and incrementing the exponent by one to obtain the normalized sum.
combinational circuits.

## Slide 14: INSTRUCTION PIPELINING
Pipeline processing can occur not only in data stream but also in
instruction stream.
An instruction pipeline reads consecutive instructions from memory while previous instructions are being executed in other segments.
This causes the instruction fetch and execute phases to overlap and perform simultaneous operations.
One possible deviation associated with such a scheme is that an instruction may cause a branch out of sequence.
In this case pipeline must be emptied and all instructions that have been read from memory after the branch instruction must be discarded.
Consider a computer with an instruction fetch and execution unit’s designed to provide a two segment pipeline.
The instruction fetch segment is implemented by means of FIFO buffer which forms a queue rather than stack.
Whenever execution unit is not using memory, control increments the program counter and uses its address value to read consecutive instructions from memory.

## Slide 15: INSTRUCTION PIPELINING
Computer with complex instructions require other phases in addition to the fetch and execute to process an instruction completely, which are given as follows:
Fetch the instruction from the memory
Decode the instruction
Calculate the effective address
Fetch the operands from memory
Execute the instruction
Store the result in proper place.
But there are certain difficulties that will prevent the instruction pipeline like
  Different segments may take different times to operate on the incoming information.
  Some segments are skipped for certain operations
Design of an instruction pipeline is most efficient if the instruction cycle is divided into segments of equal duration.
The following fig shows how the instruction cycle in the CPU can be processed
with a four segment pipeline.

## Slide 16
Fetch instruction from memory
Decode instruction and calculate effective address
Branch?
Fetch operand from memory
Execute instruction
Interrupt?
Interrupt
handling
Empty pipe
no
Update PC
yes
yes
no
Segment1:
Segment2:
Segment3:
Segment4:
Fig: Four segment CPU pipeline

## Slide 17
S
Instru
tep: | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13
ction 1 | FI | DA | FO | EX |  |  |  |  |  |  |  |  | 
2 |  | FI | DA | FO | EX |  |  |  |  |  |  |  | 
nch) 3 |  |  | FI | DA | FO | EX |  |  |  |  |  |  | 
4 |  |  |  | FI |  |  | FI | DA | FO | EX |  |  | 
5 |  |  |  |  |  |  |  | FI | DA | FO | EX |  | 
6 |  |  |  |  |  |  |  |  | FI | DA | FO | EX | 
7 |  |  |  |  |  |  |  |  |  | FI | DA | FO | EX
(Bra
Timing of instruction pipeline
Pipeline conflicts
There are three major difficulties that cause the instruction pipeline to deviate from the normal operation.
Resource conflicts  caused when two segments access the memory at the same time. (resolved by separate instruction and data memories)
Data dependency  arises when an instruction depends on the result of previous instruction, but this result is not yet available.
Branch difficulties  arises from branch and other instructions that change the value of program counter.
Four Segments FI  Fetch Instruction DA  Decode Address FO  Fetch Operand
EX  Execute Instruction

## Slide 18: RISC PIPELINING
RISC  Reduced Instruction Set Computer
One of the most important characteristics of RISC is its ability to use an efficient pipeline.
The simplicity of the instruction set can be utilized to implement an instruction pipeline using a small number of suboperations with each being executed in one clock cycle.
Because of fixed length instruction format, decoding of the operation can occur at the same time as the register selection.
All the data manipulation instructions have register to register operations. Since all the operands are in registers, there is no need to calculate effective address or fetching operands from the memory.
So Instruction pipeline can be implemented with two or three segments where
  One segment fetches the instruction from program memory.
  Other segment executes the instruction in the ALU.
  Third segment is used to store the result of the ALU operation in a destination register.

## Slide 19: RISC PIPELINING
The advantage of RISC over CISC is that RISC can achieve pipeline segments, requiring just one clock cycle while CISC uses many segments in its pipeline, with a longest segment requiring two or more clock cycles.
Another characteristic of RISC is the support given by the compiler that
translates the high level language program into machine language program.
Instead of designing hardware to handle the difficulties associated with data conflicts and branch penalties, RISC processors rely on the efficiency of the compiler to detect and minimize the delays encountered with these problems.
The following example show how a compiler can optimize the machine language
program to compensate for pipeline conflicts.

## Slide 20: DELAYED BRANCH
Clock cycles: | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10
1. Load | I | A | E |  |  |  |  |  |  | 
2. Increment |  | I | A | E |  |  |  |  |  | 
3. Add |  |  | I | A | E |  |  |  |  | 
4. Subtract |  |  |  | I | A | E |  |  |  | 
5. Branch to X |  |  |  |  | I | A | E |  |  | 
6. NOP |  |  |  |  |  | I | A | E |  | 
7. NOP |  |  |  |  |  |  | I | A | E | 
8. Instr. in X |  |  |  |  |  |  |  | I | A | E
Clock cycles: | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8
1. Load | I | A | E |  |  |  |  | 
2. Increment |  | I | A | E |  |  |  | 
3. Branch to X |  |  | I | A | E |  |  | 
4. Add |  |  |  | I | A | E |  | 
5. Subtract |  |  |  |  | I | A | E | 
6. Instr. in X |  |  |  |  |  | I | A | E
Using no-operation instructions
Rearranging the instructions
Compiler analyzes the instructions before and after the branch and rearranges the program sequence by inserting useful instructions in the delay steps

## Slide 21: VECTOR PROCESSING
There is a class of computational problems that are beyond the capabilities of a conventional computer which are characterized by the fact that they require a vast number of computations that will take a conventional computer days or weeks to complete.
In many science and engineering applications the problems can be formulated in terms of vectors and matrices that lend themselves to vector processing. Computers with vector processing capabilities are in demand in specialized applications.
The following are representative application areas where vector processing is of utmost importance
  Long-range weather forecasting
  Petroleum explorations , Seismic data analysis
  Medical diagnosis
  Aerodynamics and space flight simulations
  Artificial intelligence and expert systems , Image processing
Vector Operations
Many scientific problems require arithmetic operations on large arrays of numbers which are normally formulated as vectors and matrices of floating point numbers.

## Slide 22: VECTOR PROCESSING
A vector is an ordered set of a one-dimensional array of data items.
•
A vector V of length n is represented as a row vector by V =
{V1,V2,V3,…Vn}. It may also be represented as column vector if the data items are listed in column.
A conventional sequential computer is capable of processing operands one at a time. Consequently operations on vectors must be broken into single computations with subscripted variables.
The element Vi of vector V is written as V(I) and the index I refers to a memory address or register where the number is stored.
For example
DO 20 I = 1, 100
20 C(I) = B(I) + A(I)
This is a program for adding two vectors A & B of length 100 to produce a vector C which is implemented in a machine language as follows:
Initialize I = 0
20 Read A(I)
Read B(I)
Store C(I) = A(I) + B(I)
Increment I = I + 1 If I ≤ 100 go to 20 Continue

## Slide 23: VECTOR PROCESSING
A computer capable of vector processing eliminates the overhead associated with the time it takes to fetch and execute the instructions in the program loop.
It allows operations to be specified with a single vector instruction of the form
C(1:100) = A(1:100) + B(1:100)
The vector instruction include the initial address of the operands , the length of the
vectors, and the operation to be performed, all in one composite instruction.
The addition is done with pipeline floating-point adder. A possible instruction format for a vector instruction is as shown below:
This is essentially a three-address instruction with three fields specifying the base address of the operands and an additional field that gives the length of the data items in the vectors.
Matrix multiplication
Matrix multiplication is one of the most computational intensive operations
performed in computer with vector processors.
The multiplication of two n x n matrices consists of n2 inner products or n3 multiply- add operations. The inner product calculation on a pipeline vector processor is shown in fig: as follows:
Operation code | Base address source 1 | Base address source 2 | Base address destination | Vector length

## Slide 24: Pipeline for Inner Product
Source
A
Source
B
Multiplier pipeline
Adder
pipeline
In general the inner product consists of the sum of k product terms of the for
C = A1 B1 + A2 B2 + A3 B3 + A4 B4 + … + Ak Bk

## Slide 25: MULTIPLE MEMORY MODULE AND INTERLEAVING
•
A modular memory is useful in systems with pipeline and vector
processing.
Multiple Module Memory
Address bus
Data bus
Pipeline and vector processors often require simultaneous access to memory form two or more sources.
An instruction pipeline my require the fetching of an instruction and an
operand at the same time from two different segments.
To over come this we use memory interleaving where different sets of addresses are assigned to different memory modules.
M0 |  | M1 |  |  | M2 |  |  | M3 |  |  | 
 | AR Memory array DR |  |  | AR Memory array DR |  |  | AR Memory array DR |  |  | AR Memory array DR | 

## Slide 26: Array processors
Control Processor
A vector processor, or array processor, is a central processing unit (CPU) that implements an instruction set containing instructions that operate on one-dimensional arrays of data called vectors.
SIMD form of parallel processing is also called array processing which was
the first form of parallel processing to be studied and implemented.
The following diagram shows the structure of an array processor.
. . .
. . .
. . .
Broadcast instructions
. . .
Fig: Grid of processing elements

## Slide 27: Array processors
A two dimensional grid of processing elements executes an instruction stream that is broadcast from a central control processor.
As each element is broadcast all elements execute it simultaneously.
Each processing element is connected to its four nearest neighbors for
purposes of exchanging data.
End-around connections may be provided in both rows and columns which are not shown in figure.
In array processor each element must be able to exchange values with each of its neighbors over the path shown in fig.
Each processing element has a few registers and some local memory to
store data.
It also has a register which we can call the network register that facilitates movement of values to and from its neighbors.
ILLIAC-IV is an example of array processor which contains 64 processors with 64 bit internal structure.
CM-2
machine  processors 
accommodate up to 65536 each
processor is one bit wide.