## Slide 1: UNIT-V
MULTIPROCESSORS

## Slide 2
Characteristics of Multiprocessors
Interconnection Structures
Interprocessor Arbitration
Interprocessor Communication and Synchronization
Cache Coherence
Shared multiprocessors

## Slide 3: Characteristics of Multiprocessors
A multiprocessor system is an interconnection of two or more CPU’s with memory and input equipment.
The term processor in multiprocessor means either CPU or an IOP.
As it is most commonly defined, a multiprocessor system implies the existence of multiple CPU’s although usually there will be one or more IOP’s.
Multiprocessors are classified as multiple instruction stream and multiple data stream(MIMD) systems.
There are some similarities between multicomputer and multiprocessor
systems since both support concurrent operations.
Multiprocessing improves the reliability of the system so that a failure or error in one part has a limited effect on the rest of the system.
If a fault causes one processor to fail , a second processor can be assigned to perform the functions of the disabled processor.
So that the system as a whole can continue to function correctly with perhaps some loss in efficiency.

## Slide 4: Characteristics of Multiprocessors
One of the most important advantage of multiprocessor organization is an improved system performance.
The system derives its high performance from the fact that computations can proceed in parallel in one of the two ways:
  Multiple independent jobs can be made to operate in parallel.
  A single job can be partitioned in to multiple parallel tasks.
An overall function can be partitioned in to a number of tasks that each processor can handle individually.
System tasks may be allocated to special purpose processors whose design is optimized to perform certain types of processing efficiently.
For example is a computer system where one processor performs the computations for industrial process control, while others monitor and control various parameters such as temperature and flow rate.
Another example is a computer where one processor performs high- speed floating point mathematical computations and another takes care of routine data processing tasks.

## Slide 5: Characteristics of Multiprocessors
Multiprocessing can improve the performance by decomposing a program in to parallel executable tasks, which can be done in two ways
  User can explicitly declare that certain tasks of the program be executed in parallel.
  To provide a compiler with multiprocessor software that can automatically
detect parallelism in user’s program.
Multiprocessors are classified by the way their memory is organized.
  Multiprocessor system with common shared memory  shared or tightly coupled multiprocessor
  An alternative model of microprocessors is the distributed memory or loosely coupled systems (each processor element has it’s own private local memory).

## Slide 6: Interconnection Structures
Components that form a multiprocessor system are CPU’s , IOP’s , connected to input – output devices and a memory unit that may be partitioned in to a number of separate modules.
Interconnection between the components can have different physical configurations, depending on the number of transfer paths that are available between the processors and memory in a shared memory system or among the processing elements in a loosely coupled system.
There are several physical forms available for establishing interconnection network:
  Time – shared common bus
  Multiport memory
  Crossbar switch
  Multistage switching network
  Hypercube system

## Slide 7: Interconnection Structures
Time – Shared Common Bus
A common bus multiprocessor system consists of a number of processors connected through a common path to a memory unit.
A time – shared common bus for five processors is shown in the fig. given below.
A single shared common bus is restricted to one transfer at a time.
This means when one processor is communicating with the memory, all other processors are either busy with internal operations or must be idle
waiting for the bus.
Memory Unit
 | CPU 1 |  |  | CPU 2 |  |  | CPU 3 |  |  | IOP 1 |  |  | IOP 2 | 
Fig: Time Shared common bus organization

## Slide 8: Interconnection Structures
A more economical implementation of dual bus structure is depicted in
figure below:
Common Shared Memory
System Bus Controller
CPU
IOP
Local
Memory
System Bus Controller
CPU
Local Memory
System Bus Controller
CPU
IOP
Local Memory
Local Bus
SYSTEM BUS
Local Bus
Local Bus
Fig: System bus structure for multiprocessors
Here we have a no. of local buses each connected to its own local
memory and to one or more processors.
Each local bus is connected to CPU, an IOP, or any combination of processors.

## Slide 9: Interconnection Structures
Multiport memory
Multiport memory system employs separate buses between each
MM 1 MM 2 MM 3 MM 4
CPU 1
CPU 2
CPU 3
CPU 4
memory module and each CPU which is shown in figure with 4 CPU’s and 4 Memory Modules(MM’S) as follows:
Each processor bus is connected to each memory module.
A processor bus consists of address, data and control lines required to communicate with memory.
Memory Modules
Memory module is said to have four ports and each port accommodates one of the buses.
The module must have internal control logic to find which port will have access to memory at any given time.

## Slide 10: Interconnection Structures
Advantage of multiport memory organization is the high transfer rate that can be achieved because of multiple paths between processors and memory.
Disadvantage is that it requires expensive memory control logic and a large number of cables and connectors.
Crossbar Switch
It consists of a no. of crosspoints that are placed at intersections between processor buses and memory module paths.
MM1
CPU1
CPU2
CPU3
CPU4
Memory modules
MM2
MM3
MM4
Figure beside shows the crossbar switch interconnection between four
CPU’s and four memory modules.
The small square in each crosspoint is a switch that finds the path from a processor to a memory module.
Each switch point has control logic to set up the transfer path between a processor and memory.

## Slide 11: Interconnection Structures
The circuit consists of multiplexers that selects the data, address and control from one CPU for communication with the memory module.
Priority levels are established by the arbitration logic to select one CPU
when two or more CPU’s attempt to access the same memory.
A crossbar switch organization supports simultaneous transfers from all memory modules because of separate path associated with each MM.
The following figure shows the (block diagram) functional design of crossbar switch connected to one` memory module.
Fig: Block Diagram of Crossbar Switch
Memory Module
data address R/W
memory enable
}
}
}
}
data,address, and control from CPU 1
data,address, and control from CPU 2
data,address, and control from CPU 3
data,address, and control from CPU 4
Multiplexers and arbitration logic

## Slide 12: Interconnection Structures
two-output
The 2 x 2 interchange switch has two inputs labeled A and B and two
outputs labeled 0 and 1.
There are control signals (not shown) associated with the switch that establish interconnection between input and output terminals.
B
A connected to 0
A A
B
0 0
1 1
A connected to 1
A
B
0
1
B connected to 0
A
B
0
1
B connected to 1
Multistage Switching network
The basic component of this network is a two-input, interchange switch as shown in fig below:
Fig: Operation of 2 x 2 Interchange Switch

## Slide 13: Interconnection Structures
The switch
has the
capability
of connecting
input A to either of the
outputs. Terminal B of the switch behaves in a similar fashion.
also has the to arbitrate conflicting
Switch capability between requests.
If inputs A and B both
request the same output
terminal only one of them will be connected, other will be blocked.
In omega switching network
configuration there is
exactly one path from each
source to any particular
destination.
0
1
000
001
0
1
010
011
0
1
100
101
0
1
110
111
0
1
0
1
0
1
P1
P2
Fig: A binary tree with 2 x 2 s
witches
Fig; 8x8 Omega Switching Network
0
1
2
3
4
5
6
000
001
010
011
100
101
110

## Slide 14: Interconnection Structures
Hypercube interconnection
Hypercube or binary n-cube multiprocessor structure
is a loosely
coupled system composed of N = 2n processors interconnected in an n- dimensional binary cube.
Each processor forms a node of the cube.
Each processor has direct communication paths to n other neighbor processors which corresponds to the edge of the cube.
There are 2n distinct n-bit binary addresses that can be assigned to the
processors.
Each processor address differs from that of each of its n neighbors by exactly one bit position.
The hypercube structure for n = 1, 2, 3 is represented as in the figure as
follows:
  Once cube structure  n = 1 and 2n =2
  Two cube structure  n = 2 and 2n = 4

## Slide 15: Interconnection Structures
One-cube Two-cube Three-cube
A two cube structure has four nodes interconnected as a square.
A three cube structure has eight nodes interconnected as a cube.
An n cube structure has 2n nodes with a processor residing in each node.
Each node is assigned with a binary address in such a way that the address of two neighbors differ in exactly one bit position.
For example:
  Three neighbors of the node with address 100 in a three-cube structure are 000, 110, 101.
  Each of these binary numbers differs from the address 100 by one bit value.
11
01
0
1
00
10
010
110
011
111
101
100
001
000

## Slide 16: Interprocessor Arbitration
CPU contains a no. of internal buses for transferring information between processor registers and ALU.
A memory bus consists of lines for transferring data, address, and read/write information.
An I/O bus is used to transfer information and from input and output
devices.
A bus that connects major components in a multiprocessor system such as CPU’s , IOP’s and memory is called a system bus.
The processors in a shared memory multiprocessor system request access to common memory or other common resources through the system bus.
If another processor is currently utilizing the system bus, requesting processor must wait.
Arbitration must then be performed to resolve this problem.
Arbitration logic would be part of the system bus controller placed between the local bus and system bus.

## Slide 17: Interprocessor Arbitration
System Bus
A system bus consists of approximately 100 signal lines which are divided in to three functional groups Data, Address and Control (in addition there are power distribution lines that supply power between components)
  For example the IEEE standard 796 multibus system has 16 data lines, 24 address lines, 26 control lines, and 20 power lines for a total of 86 lines.
  Data transfers over the system bus may be synchronous or asynchronous
  In synchronous bus each data item is transferred during a time slice
know in advance to both source and destination units.
  Synchronization is achieved by driving both units from a common clock source.
  In asynchronous bus each data item being transferred is accompanied by handshaking control signals to indicate when data are transferred from source and received by the destination

## Slide 18: Interprocessor Arbitration
PI Bus PO
arbiter 1
PI Bus PO
arbiter 2
PI Bus PO
arbiter 3
PI Bus PO
arbiter 4
Serial arbitration procedure
Arbitration procedure service all processor requests on the basis of the established priorities.
A hardware bus priority resolving technique can be established by means of a serial or parallel connection of the units requesting control of the system bus.
Serial priority resolving technique is obtained from Daisy-chain connection of bus arbitration circuits similar to the priority interrupt logic.
The device closest to the priority line is assigned the highest priority.
The following figure shows the daisy-chain connection of four arbiters. It is assumed that each processor has its own bus arbiter logic with priority-in and priority-out lines
Highest
priority
1
To next arbiter
Bus busy line
Fig: serial arbitration

## Slide 19: Interprocessor Arbitration
Parallel Arbitration Logic
The parallel bus arbitration technique uses an external priority encoder and a decoder as shown in figure follows:
Bus arbiter 1
Ack Req
Bus arbiter 2
Ack Req
Bus arbiter 3
Ack Req
Bus arbiter 4
Ack Req
Bus busy line
4 x 2 Priority encoder
2 x 4 Decoder
Each bus arbiter in parallel scheme has a bus request output line and a
bus acknowledge input line.
Each arbiter enables the request line when its processor is requesting access to the system bus.

## Slide 20: Interprocessor Arbitration
The processor takes the control of the bus if its acknowledge input line is enabled.
The bus busy line provides an orderly transfer of control, as in daisy- chaining case.
In the figure, the request lines from four arbiters going in to a 4 x 2
priority encoder.
The output encoder generates a 2-bit code which represents the highest priority unit among those requesting the bus.
The truth table of the priority encoder output drives a 2 x 4 decoder which enables proper acknowledge line to grant bus access to the highest priority unit.
The two bus arbitration procedures just described use a static priority algorithm since the priority of each device is fixed by the way it is connected to the bus.
In contrast the dynamic priority algorithm gives the system the capability for changing the priority of the devices while the system is in operation.

## Slide 21: Interprocessor Communication & Synchronization
Various processors in a multiprocessor system must be provided with a facility fro communicating with each other.
A communication path can be established through the common input- output channels.
In a shared memory multiprocessor system most common procedure is
to set aside a portion of memory that is accessible to all processors.
Primary use of this common memory is to act as a message center similar to a mailbox where each processor can leave messages for other processors and pickup messages intended for it.
The sending processor structures a request, a message, or a procedure and places it in the memory mailbox.
Status bits residing in the common memory are generally used to indicate the condition of the mailbox.
The receiving processor can check the mail box periodically to find if there are valid messages for it, where the response time is consuming.

## Slide 22: Interprocessor Communication & Synchronization
A more efficient procedure is for the sending processor to alert the receiving processor directly by means of an interrupt signal.
This is done through a software-initiated interprocessor interrupt by means of instruction in the program of one processor which when executed produces an external interrupt condition in a second processor.
There are three organizations that have been used in the design of Operating System(OS) for multiprocessors:
Master – slave configuration:
  In this mode one processor designated as master always executes the OS functions.
  Other processors denoted as slave do not executes the OS functions. if any slave processor wants to execute OS function, it sends a request by interrupting the master.
Separate Operating System:
  In this organization each processor can execute the operating system routines it
needs. Suitable for loosely coupled system.
Distributed Operating System:
  In this organization OS routines are distributed among the available processors.

## Slide 23: Interprocessor Communication & Synchronization
Interprocessor Synchronization
The instruction set of a multiprocessor contains basic instructions that are used to implement communication and synchronization between cooperating processes.
Communication refers to the exchange of data between different
processes.
Synchronization refers to the special case where the data used to communicate between processors is control information.
Synchronization is needed to enforce the correct sequence of processes
and to ensure mutually exclusive access to shared writable data.
A number of hardware mechanisms for mutual exclusion have been developed, among them one of the most popular method is through the use of binary semaphore.
The mechanism that will guarantee the orderly access to shared memory and other share resources which is necessary to protect data from being changed simultaneously by two or more processors is called Mutual Exclusion.

## Slide 24: Interprocessor Communication & Synchronization
Mutual exclusion must be provided in a multiprocessor system to enable one processor to exclude or lock out access to a shared resource by other processors when it is in a critical section.
Critical section is a program sequence that once begun must complete
execution before another processor accesses the same shared resource.
A binary variable called as semaphore is often used to indicate whether or not a processor is executing a critical section.
If the binary semaphore value is
  1  A processor is executing a critical section, that not available to other processors
  0  Available to any requesting processor
Testing and setting a semaphore
R  M[SEM] M[SEM]  1
/ Test semaphore /
/ Set semaphore /

## Slide 25: CACHE Coherence
Shared data leads to another problem in a multiprocessor system where the presence of multiple caches means that copies of shared data may reside in several caches.
When any processor writes to a shared variable in its own cache all other caches that contain a copy of that variable will then have the old, incorrect value.
They must be informed of the change so that they can either update their copy to the new value or invalidate it.
Cache coherence is defined as the situation in which all the cached copies of shared data have the same value at all times.
There are two basic approaches for performing write operations on data in a cache :
  Write through  changes the data in both main memory and cache
  Write back  changes the data only in the cache memory not in the main memory.
Similar approaches are used in multiprocessor systems.

## Slide 26: CACHE Coherence
A write through protocol is implemented in two fundamental versions. One version is based on updating the values in other caches, while the second relies on invalidating the copies in other caches.
In write-back protocol multiple copies of a cache block may exist if different processors have loaded (read) the block in to their caches.
If some processor wants to change this block, it must first become an exclusive owner of this block.
Snoopy caches
If two processors want to write to the same cache block at the same time, one of the processors will be granted the use of the bus first and will become the owner.
As a result the processors copy of the cache block will be invalidated.
The second processor can then repeat its write request. This sequential handling of write requests ensures that two processors can correctly change different words in a given cache block.
It is done based on the ability of cache controllers to observe the activity on the bus and take appropriate actions, we refer this as snoopy cache.

## Slide 27: Shared memory multiprocessors
Caches
Caches
Caches
Multiple processors connected to a single centralized memory – since all processors see the same memory organization  Uniform Memory Access (UMA)
In shared-memory multiprocessors all the processors can access the
entire memory address space.
Implicit communication is possible.
Transfer of data between processor is usually implicit.
Processor Processor Processor Processor
Caches
Main Memory
I/O System

## Slide 28: (UMA) Uniform-memory-access Shared-memory System
Interconnection Network
Memory
CPU
Memory
CPU
Memory
CPU